## Slide 1
Vincent Moreau, Manuela Profir, CRS4
10-04-24
3rd Technical Review Meeting
WP2.1 Deformed bundle simulation
Blind pre-tests
Advanced Nuclear Safety Evaluation of Liquid Metal Using Systems

## Slide 2
CAD provided by ENEA
Almost CFD grade and directly uploaded in STARCCM+ 3D-CAD
Reworked in STARCCM+ 3D-CAD
Methodology should be adaptable to an “unknown” deformation shape
Pre-test simulations

## Slide 3
CAD provided by ENEA
Reworked in STARCCM+ 3D-CAD
Pre-test simulations
Bright idea allowing to reduce the computational domain!

## Slide 4
CAD provided by ENEA
Reworked in STARCCM+ 3D-CAD: some parts simplified
Pre-test simulations

## Slide 5
STARCCM+ geometry
From the lateral intake to ~13 cm above the active region
Structures: only the pin simulator bundle active part
Pre-test simulations

## Slide 6
STARCCM+ 3D-CAD geometry
Region / mesh organization: 1-low fluid domain, 2- Intake extension, 3- Convergent extension
Pre-test simulations

## Slide 7
STARCCM+ geometry
Organization: 1) around spacer, 2) Active part and 3) Outflow
Pre-test simulations

## Slide 8
TCs position
TCs moved from C1 to B1 as well as from E3 to D6
They are placed at 2 measurement planes (Z=300mm and Z=500mm)
Pre-test simulations

## Slide 9
TCs position
Probes location for data extraction
Pre-test simulations

## Slide 10
Three cases under investigation
Numerical setting inherited from pre-pre-tests
Same mesh for all three cases
Pre-test simulations
Case | Inlet T (C) | Flowrate (kg/s) | Power (kW) | dT (K) | Riser mean wall Y+
3A | 400 | 19.0 | 222 | 80 | 2.2
4A | 400 | 12.7 | 222 | 120 | 1.7
7A | 400 | 5.0 | 29 | 40 | 0.7

## Slide 11
TCs position issue
Numerical probes give mean cell temperature
TCs tend to be larger than the cell size
Embedded TCs are 0.35 mm wide
The clad DT is about 11 K over 0.35 mm.
A mismatch of 0.1 mm is 3 K!
Uncertainty, both experimental and numerical may be much higher than foreseen
As an attempt to minimize the numerical measure error, we create a 0.35 mm wide external clad layer.
Similar issue for the 0.5 mm wide bulk TCs
Pre-test simulations

## Slide 12
TCs position issue
Similar issue for the 0.5 mm wide bulk TCs
Profile T between Pin 1 and Pin5 (3mm).
Lead => No real bulk temperature
Very sensitive to the exact TC position.
Pre-test simulations

## Slide 13
Effect of thermal conductivity
Only matters when there is a large transverse thermal flux: i.e. only deformed pins and neighbors.
Boron Nitride more resistive at higher temperature.
Difference with steel is higher for Case 4A and reaches ~5 K at TC 31 – 76.
The uncertainty on the BN thermal conductivity may impact the TC measure by a few K.
Pre-test simulations
TC 31

## Slide 14
Simulation results: mesh sensitivity on Case 3A
Very similar results on selected TCs but denser 2D mesh chosen because: lower Y+ and still quite manageable for steady simulations.
Pre-test simulations
Case3A Ref. 4, 200, 1.5 mm 300 Layers Active 6 BL Active Riser 0.3 mm 0.3 mm, 6 BL Note
Pressure drop active [kPa] 9.99 9.97 10.11 9.60 9,88
Pressure drop Inlet-Outlet [kPa] 31.01 31.01 31.30 30.49 30.99
Mean Active Pin Wall Y+ 9.8 9.8 3.5 5.5 2.2
TC 07 A5 mid 412.6 412.7 412.9 413.3 413.3 Wrapper
TC 52 A5 up 420.2 420.3 419.8 420.5 420.2 ‘’
TC 14 D6 mid 432.6 432.9 433.3 432.9 433.0 Bulk
TC 59 D6 up 461.0 460.9 461.5 460.2 460.9 ‘’
TC 19 B2-B3 mid 450.9 451.4 451.2 450.5 450.5 Channel
TC 64 B2-B3 up 490.8 491.1 491.1 492.4 491.9 ‘’
TC 15 D2-D6 mid 446.9 447.3 447.0 446.1 446.3 ‘’
TC 60 D2-D6 up 478.3 478.4 478.1 477.1 477.3 ‘’
TC 31 04-13 mid 492.1 492.0 492.6 492.4 492.2 Front Pin 13
TC 76 04-13 up 520.3 520.4 521.2 522.5 522.2 ‘’
TC 40 07-19 mid 477.3 477.4 476.9 475.8 475.4 Front Pin 19
TC 85 07-19 up 507.9 507.9 507.3 506.2 505.9 ‘’
Riser Fluid Mesh [k] 2,677 3,863 3,345 5,566 6,665
Whole Mesh [k] 7,061 9,500 7,756 12,853 14,030

## Slide 15
Simulation results: Case 4A, appearance of a low temperature instability
Relevant only in sector C5
Same if riser layers increased from 200 to 300 => could likely be related to a flow instability
Pre-test simulations

## Slide 16
Simulation results: Case 3A and 4A, effect of the spacer
Regularizing the flow asymmetry. Taken 5 mm below and 5 mm above the spacer
Pre-test simulations
4A, 12.7 kg/s
3A, 19 kg/s
7A, 5kg/s
Below
Above

## Slide 17
Simulation results: Case 3A and 7A, Vertical velocity along active part
Lower velocity in the smaller channels. Hysteresis effect when deformation is over.
Pre-test simulations
30 cm
60 cm
50 cm
3A, 19 kg/s
7A, 5 kg/s

## Slide 18
Simulation results: Case 3A and 7A, Clad external temperature
Maximum on top in deformed pins
Combined effect of slower flow and of a smaller channel feed by the same heat flux
Pre-test simulations
3A, 19 kg/s
7A, 5 kg/s

## Slide 19
Simulation results: Case 3A and 7A, Clad external temperature
Maximum on top in deformed pins
Combined effect of slower flow and of a smaller channel feed by the same heat flux
Pre-test simulations
3A, 19 kg/s
7A, 5 kg/s

## Slide 20
Conclusions
    The pre-tests simulations have been performed without particolar complication
    The very high thermal gradients makes the TC positioning and temperature interpretation very challenging
    The BN thermal conductivity and its temperature dependence impact the clad temperature in case of transversal heat flux
    The maximum clad temperature arise at the top of the deformed pins
    It is caused by the combined effect of slower flow and of a thinner channel
    No particular issue is forseen for the conduction of the experiment.
Pre-test simulations

## Slide 21
References
    MMMD Hussain & V Moreau (2023). Appendix to Deliverable D2.2 HELENA deformed bundle pre-pre-test simulations
Verification Study